## Slide 1
10-STEP GIS FOOTPRINT WORKFLOW
• Project Phase 1: Automated image telemetry processing.
• Steps 1-4 (Collection & Extraction):
  - Raw images from DJI drone flight are collected (Step 1).
  - ExifTool parses binary EXIF metadata automatically (Step 2-4).
  - Extracts: GPS location (Lat/Lon/Alt), flight height, and yaw/pitch orientation.
• Steps 5-6 (FOV Calculation):
  - Physical sensor specifications are mapped to compute horizontal/vertical FOV.
• Steps 7-8 (Ground Footprint Corners Projection):
  - Combines camera viewing angles, drone altitude, and yaw rotation coordinates.
• Steps 9-10 (Polygon Building & GIS Export):
  - Loops coordinates as a polygon, and exports footprints in WGS 84 GeoJSON.

## Slide 2
CAMERA FIELD OF VIEW & COVERAGE MATH
• Camera parameters: Focal length (f = 3.61 mm), Sensor width (Sw = 6.17 mm).
• Sensor Height aspect crop adjustment:
  - Widescreen 16:9 images (4000x2250) crop the physical 4:3 sensor (4.55 mm).
  - Effective sensor height: Sh = 6.17 * (2250 / 4000) = 3.47 mm.
• Step 6: Calculating viewing angles (FOV):
  - Horizontal FOV = 2 * arctan(Sw / (2 * f)) = 81.03°
  - Corrected Vertical FOV = 2 * arctan(Sh / (2 * f)) = 50.64° (instead of 64.44°)
• Step 7: Ground footprint dimensions (at nadir/straight-down):
  - Width = 2 * Altitude * tan(Horizontal FOV / 2) ≈ 1.71 * Altitude
  - Corrected Height = 2 * Altitude * tan(Vertical FOV / 2) ≈ 0.96 * Altitude (instead of 1.28)
• Step 8: 2D Rotation using Yaw Orientation:
  - X_rot = X_local * cos(yaw) + Y_local * sin(yaw)
  - Y_rot = -X_local * sin(yaw) + Y_local * cos(yaw)

## Slide 3
COORDINATE REFERENCE SYSTEMS & PROJECTIONS
• Global Reference System: Drone images log coordinates in WGS 84 (EPSG:4326) degrees.
• Flattening Map System: Calculations (meters) require projecting to UTM grid.
• UTM Zone 15N (EPSG:32615) covers Duluth, Minnesota area.
• OGR Coordinate Transformations (in C++ App):
  - Translates UTM 15N to standard spherical GPS coordinates for GeoJSON export.
  - Translates UTM 15N to UTM 10N (EPSG:32610) to query the dsm.tif GeoTIFF elevation raster.
• Robust Parsing: Validates numeric data when reading point cloud text blocks and skips text headers (X,Y,Z) to prevent (0,0) coordinate origin drift.

## Slide 4
INTERACTIVE MAP VISUALIZERS (C++ & PYTHON)
• Interactive 3D Canvas: Renders point cloud (color-coded by height), flight nodes, and footprints.
• Dynamic Photo Warping Overlay:
  - Applies QTransform matrix to translate, rotate, and scale photos over the point cloud.
• GDAL Elevation Querying:
  - Queries float32 elevation values from dsm.tif raster in real-time under the mouse cursor.
• Dynamic UI sidebar layout (Qt6 Widget structures):
  - Dynamic list selection connects photo markers directly to metadata table.
  - ScrollArea wrapper prevents layout clipping on small monitors.
  - QTableWidget details every EXIF metadata tag (copyable via Ctrl+C).

## Slide 5
UAV METADATA STANDARDS & FAIR PRINCIPLES
• Research Objective: Compare metadata schemas to ensure UAV data interoperability.
• Why Metadata Standards Matter: Drone missions produce heterogeneous formats. Standardized tags ensure files are easily discovered and loaded.
• FAIR Principles for Drone Data:
  - Findable: Standard search terms and unique IDs.
  - Accessible: Files are open and queryable through API catalogs.
  - Interoperable: Common schemas allow direct import into QGIS, ArcGIS, or Python.
  - Reusable: Complete details on sensor calibration and coordinates.
• Key Barrier: Traditional XML schemas (ISO) are heavy, while raw vectors (GeoJSON) lack rich sensor calibration attributes.

## Slide 6
GEOGRAPHIC METADATA: ISO 19115 & ISO 19139
• ISO 19115 (Metadata Schema): The cornerstone international standard for geographic metadata.
  - Defines elements describing geographic datasets (spatial range, data quality, lineage, sensor).
• ISO 19139 (XML Schema Implementation):
  - Details how ISO 19115 elements must be structured inside XML files for machine exchanges.
• OGC (Open Geospatial Consortium) Standards:
  - Standardizes services like CSW (Catalog Service for Web) to publish and search ISO XML documents.
• Main Limitation: Complex XML encoding makes them difficult for cloud software and web APIs to read rapidly.

## Slide 7
CLOUD-OPTIMIZED FORMATS (COG & COPC)
• GeoTIFF vs. Cloud Optimized GeoTIFF (COG):
  - Standard GeoTIFF has to be read entirely to query an elevation point.
  - COG organizes elevation cells into HTTP range request tiles.
  - Allows GIS apps to query terrain elevation in milliseconds over a network without downloading the full gigabyte file.
• LAS/LAZ vs. Cloud Optimized Point Cloud (COPC):
  - LAZ files are compressed point clouds but lack spatial indexes.
  - COPC structures point clouds as an octree layout inside a LAZ file.
  - Enables streaming of points based on resolution and bounding boxes.

## Slide 8
SPATIOTEMPORAL ASSET CATALOG (STAC)
• STAC Specification: A modern JSON-LD metadata standard built to catalog geospatial assets (photos, DEMs, point clouds).
• Three core components in the STAC hierarchy:
  - STAC Catalog: The root JSON file indexing the structure.
  - STAC Collection: Groups related UAV images, documenting camera specs, focal length, and spatial boundaries.
  - STAC Item: GeoJSON-based metadata document describing a single image, linked to the raw JPG asset.
• STAC API: Defines a standard RESTful query API to search drone photos by time ranges and footprint bounding boxes.

## Slide 9
COMPARATIVE ANALYSIS FOR UAV INTEROPERABILITY
• ISO Standards: Heavyweight, structured for formal catalogs, but difficult to implement for single uav frames.
• GeoJSON: Excellent vector format for footprints, but lacks metadata tags for camera calibration and gimbal angles.
• STAC: Combines the best of both worlds. Represents footprints in GeoJSON while storing rich camera assets and flight telemetry in structured JSON-LD properties.
• Recommendation for UAV GIS Workflows:
  - Store raw telemetry in STAC Items.
  - Export footprint boundaries as GeoJSON features.
  - Stream elevation and point clouds via COG and COPC.